Work with Firefox with BBB.
You use the IP address 192.168.7.2 to connect to the BBB (once you connect your BBB over ethernet and power).
Then click on Cloud9 section of that page, and then click again on another link of Cloud9.
+ > Linux Terminal to see a terminal for BBB.

You want to get the ip address of the BBB by doing ifconfig. Check the one over ethernet (starts with eth).

Connect over your BBB using ssh in your terminal with your IP address.

Default login: root with no password.

Now, you can code in python from there using:
nano test.py
Then:
python test.py

You need to know which version of python you are running on your BBB.

Pins for digital write are the ones in green in the sketch that is in this directory.
P9_30 → under p9 header at pin 30.

There are two headers: P8, P9.

For Python to communicate with GPIO pins:
import Adafruit_BBIO.GPIO as GPIO

Get our pin and set it as output:
outPin=”P9_12”
GPIO.setup(outPin, GPIO.OUT)

If you want to put delays:
from time import sleep

for x in range(0,5):
GPIO.output(outPin, GPIO.HIGH)
sleep(3)
GPIO.output(outPin, GPIO.LOW)
sleep(3)

This resets the pins to use them later (?). Without it, we could get an error next time we run it:
GPIO.cleanup()

If you want to play with analog, include this package:
import Adafruit_BBIO.PWM as PWM

Then set your pin:
myPWM=”P8_13”
# duty cycle set to 0% - signal off all the time. 100Hz
PWM.start(myPWM, 0, 1000)

To change your duty cycle, you can do:
#DC is some duty cycle value from 0 to 100% you want to put
PWM.set_duty_cycle(myPWM, DC)

Otherwise, you can convert a voltage value that you take as input from your program into a duty cycle value by doing the following:
DC = V//3.365*100
if DC>100:
DC=100

Once you are done, you can do:
#Stops pin with PWM
PWM.stop(myPWM)
PWM.cleanup()

You can set the frequency doing the following:
PWM.set_frequency(myPWM, 100)

Overall, this is how the program looks:

import Adafruit_BBIO.PWM as PWM

myPWM = “P8_13”
PWM.start(myPWM, 0, 1000)

for i in range(0,5):
V=input(“Taking voltage val: “)
DC=V/3.365*100
if DC>100:
DC=100
PWM.set_duty_cycle(myPWM, DC)
PWM.set_frequency(myPWM, 100)
PWM.stop(myPWM)
PWM.cleanup()

To read analog values (blue pins on images):
import Adafruit_BBIO.ADC as ADC
# activate the analog to digital converter pins
ADC.setup()
# import for delays in program
from time import sleep
analogPin=”P9_33”

while(1):
# read from analog pin
potVal=ADC.read(analogPin)
#converts your value to volts
potVolts=potVal*1.8 # 1.8 was the maximum of his potentiometer

GPS project part 1:
import serial
import Adafruit_BBIO.UART as UART
#P9_UART1TX and P9_UART1RX are activated from this (because this is UART1)
UART.setup("UART1")
# Serial port communicating with the GPS. Path to device from the BBB is /dev/ttyO1
# Baud rate: 9600
GPS = serial.Serial('/dev/ttyO1', 9600)
while(1):
# wait for the GPS info
        while GPS.inWaiting()==0:
        pass
# get string value
        NMEA=GPS.readline()
        print NMEA

Communication of Arduino and BeagleBone Black over SPI:
http://ulasdikme.com/projects/arduino/BBB_Arduino_SPI.php

This link shows the connections that need to be made between the arduino and the beaglebone black so that they can communicate. The tutorial however is clearly not the best.

This sets up SPI for our BeagleBone Black:
https://learn.adafruit.com/setting-up-io-python-library-on-beaglebone-black/spi
And in there is also the commands to accept SPI1 to change the uEnv.txt file.

This shows you basic operations of the SPI library:
https://github.com/adafruit/adafruit-beaglebone-io-python/blob/master/docs/SPI.rst

My guess is :
spi = SPI(0,0)
spi.open(0,0)
spi.writebytes([33])
spi.close()
spi.open(0,0)
spi.readbytes(10)
spi.close()

Source code for spi library:
https://github.com/adafruit/adafruit-beaglebone-io-python/blob/master/source/spimodule.c

This seems to take the camera input with python:
https://stackoverflow.com/questions/50227719/accessing-beaglebone-python-opencv-usb-camera-but-the-display-showing-black-scre

What I learned is that VideoCapture is pretty slow from this post: https://stackoverflow.com/questions/37169517/beaglebone-black-opencv-python-is-too-slow (do I see a suggestion in the second post?). We can thread the process:
https://www.pyimagesearch.com/2015/12/21/increasing-webcam-fps-with-python-and-opencv/

This talks about how to install opencv-python for the beaglebone black:
http://mrityunjai.in/installing-opencv-2-4-9-in-beagleboneblack-ubuntu-14-04/
(You have to make it :O )

Using edge detection filter, seems pretty easy. However, might need to apply Gaussian filter as well, because if there are patterns on the floor, could get the robot f* up… Might need to look up for a horizontal line, or a big line that delimits the floor from the wall:
https://bigfacerobotics.wordpress.com/2014/12/18/obstacle-detection-using-opencv/

If the edge is too close to the lower end of the image, turn around… Or, if you see the edge in one frame and do not see it in another, this means you need to back up (if too close) or turn around.

Could have both a ultraviolet sensor and a webcam to identify if too close of an obstacle. We could have some speech telling which took the decision… (ultraviolet or webcam?)

https://pythonprogramminglanguage.com/text-to-speech/ seems pretty easy to use… once pip is installed and the package as well hahaha